## Slide 1: Current Sensor Deployment
© 2025 Yuseop Sim, All rights reserved.

## Slide 2: Part 1 Locate Current Sensor Code File
© 2023 Yuseop Sim, All rights reserved.
1. Drag and drop the "CT_ADC_Current_Pipeline" file to/home/pi via WinSCP. The file is in OneDrive: Martin Byung-Guk Jun's files - JUNLAB\6. Educational Materials\[EK, YS] Sensor installation
2. Follow “[Trixie] MQTT Setup” slides located in “Martin Byung-Guk Jun's files - JUNLAB\6. Educational Materials\[EK, YS] Sensor installation” and finish the MQTT setup

## Slide 3: Part 2 Install Sound Pipeline Requirements
1. Update packages:
sudo apt update
2. Install Python and current sensor requirements:
sudo apt install -y \
python3 \
python3-serial \
python3-paho-mqtt
Notes: -y : automatic approve to install

## Slide 4: Part 3 CT & ADC Hardware Installation
Clamp a Current Transducer (CT) on a desired wire.
Wire the CT to an ADC USB device
Connect the ADC to a Pi
Verify ADC python3 -m serial.tools.list_ports –v
Notes: dtoverlay=vc4-kms-v3d,audio=off~
2. Disable bcm soundcard & vc4
cd /etc/modprobe.d
sudo nano alsa-blacklist.conf
type 'blacklist.conf
blacklist snd_bcm2835
blacklist snd_soc_hdmi_codec
blacklist snd_soc_core
blacklist snd_soc_simple_card_utils
blacklist vc4'
ctrl+o & Enter, ctrl+x,
sudo update-initramfs -u
sudo reboot

## Slide 5: Part 4-1 Crontab Setting (Single Channel Use)
© 2023 Yuseop Sim, All rights reserved.
MQTT_USER="lamm-machine_name-raspi"
MQTT_PASSWORD="1101"
EQUIPMENT_NAME=“machine_name"
# Current Sensor Settings
CURRENT_CHANNELS="CH4"
CURRENT_CH4_CT_V_FULL="5.0"
CURRENT_CH4_CT_I_FULL="50.0"
CURRENT_CSV_ENABLED=true
CURRENT_NOISE_FLOOR_ENABLED=true
CURRENT_NOISE_FLOOR_A="0.01"
CURRENT_NOISE_FLOOR_MODE="zero"
# Current Pipeline
@reboot sleep 20 && cd /home/pi/CT_ADC_Current_Pipeline && /usr/bin/python3 -m current >> /home/pi/CT_ADC_Current_Pipeline/current.log 2>&1
2. Crontab setting for a single ADC channel use:
1. Access the crontab setting
crontab -e
Can be true or false: True: save csv files
False: do not save
Noise attenuation option: Some ADCs give noise even if a machine is off
Anything highlighted in this color means they need to be changed by a user

## Slide 6: Part 4-2 Crontab Setting (Multiple Channels Use)
© 2023 Yuseop Sim, All rights reserved.
# Current Sensor Settings
CURRENT_CHANNELS="CH4, CH5”
CURRENT_CH4_CT_V_FULL="5.0"
CURRENT_CH4_CT_I_FULL="50.0"
CURRENT_CH5_CT_V_FULL=“3.0"
CURRENT_CH5_CT_I_FULL="50.0"
2. Crontab setting for multiple ADC channels use (only change this section):
1. Access the crontab setting
crontab -e

## Slide 7: Part 5 Collect Current Data
© 2023 Yuseop Sim, All rights reserved.
Restart Pi
sudo reboot
2. Navigate to /home/pi/CT_ADC_Current_Pipeline/current_data/machine_name/ and there will be channel folder(s). Retrieve a current CSV file and, on Windows, open and inspect it
Notes: 127.0.0.1 = Local host, loop-back address
Port 5000 : normally used to develop or test a web application

## Slide 8: Part 6 Verify MQTT Topics
1. Current RMS subscription for all channels
mosquitto_sub -h localhost \
-u 'lamm-machine_name-raspi' \
-P '1101' \
-t 'machine_name/current/#' \
-q 1 -v
2. Current RMS subscription for a single channel / one channel from a multi-channel configuration
mosquitto_sub -h localhost \
-u 'lamm-machine_name-raspi' \
-P '1101' \
-t 'machine_name/current/ch#/rms' \
-q 1 -v
Types of all topics:
machine_name/current/
│
├── ch#
│ ├── rms
│ └── voltage
│
├── metadata
├── status
│
├── control
│ └── csv
│
└── status
└── csv
Notes: https://aruljohn.com/blog/raspberry-pi-sync-time/